/**
@defgroup XBT_API      XBT
@brief The core toolbox of SimGrid, containing useful datatypes and friends
*/

/**
@defgroup TRACE_API TRACE
@brief Tracing mechanism and its functions.

SimGrid can trace the resource (of hosts and links) utilization using
any of its programming interfaces (MSG, SimDAG and SMPI). This means
that the tracing will register how much power is used for each host
and how much bandwidth is used for each link of the platform.

The idea of the tracing facilities is to give SimGrid users to
possibility to classify MSG and SimDAG tasks by category, tracing the
platform utilization (hosts and links) for each of the categories.
The API enables the declaration of categories and a function to
associate them to the tasks (MSG and SD). The tasks that are not
classified according to a category are not traced. If no categories
are specified, simulations can still be traced using a special
parameter in the command line (see \ref outcomes_vizu for details).
*/


/** \defgroup SIMIX_API      SIMIX
    \brief POSIX-like interface for building simulation

    This is a developer-level interface that should be useful only if you
    plan to design a new interface for SimGrid.
*/



/**
@defgroup SURF_API SURF
@brief Internal kernel of all the simulators used in SimGrid, and associated models.

SURF provides the core functionnalities to simulate a virtual
platform. It is very low-level and is not intended to be used by end
users, but rather to serve as a basis for higher-level simulators. Its
interfaces are not frozen (and probably never will be), and the
structure emphasis on performance over ease of use. This module
contains the platform models. If you need a model that is not encoded
yet, please come to the devel mailing list so that we can discuss on
the feasibility of your idea.

Please note that as it is not really intended for public use, this
module is only partially documented.
*/